## Slide 1: Sensor Fusion – Accurate Estimation of Gravity and Linear Acceleration
Ramasamy Kannan
ram.kannan@samsung.com

## Slide 2: Introduction
Accelerometer Sensor data is combination of linear acceleration and gravity components. Applications would more be interested in using linear acceleration and gravity sensor data separately.
Accelerometer data is used for correcting the tilt (roll and pitch) orientation measurements generated from the gyroscope using Sensor Fusion.
The gravity measurements in 3D space are derived from the orientation (pitch, roll and yaw) measurements that is output from the Kalman filter.
The linear acceleration measurements in 3D space are then derived by removing the gravity components from the calibrated accelerometer measurements.
By using corrected tilt measurements from the Kalman filter, it is ensured that the accurate gravity and linear acceleration data is derived.

## Slide 3: Computation of Gravity and Linear Acceleration
Sensor Fusion - Orientation Estimation
Accelerometer
Magnetometer
Gyroscope
Gravity Computation
Linear Acceleration Computation
Tilt (Φ, θ)
(Gx,Gy,Gz)
(LAx,LAy,LAz)
(Ax,Ay,Az)

## Slide 4: Gravity
Gravity virtual sensor data provides the measure of the direction in which the earth’s gravitational force is observed in the device’s frame of reference.
The orientation of the device decides the measure of the influence of earth’s gravitational force on the 3-axes of the device.
Accurate Orientation data taken from the output of the Orientation Estimation phase is used to compute Gravity virtual sensor data. The projection of the tilt (pitch, roll) on the gravity axis is used to determine gravity on particular axis.
Gx = EARTH’s GRAVITY * -sin(pitch);
Gy = EARTH’s GRAVITY * -sin(roll);
Gz = EARTH’s GRAVITY * cos(pitch) * cos(roll);
When a device the tilt (pitch, roll) is changed from (0, 0) to (π/2, 0), phone is rotated around y-axis, the x-axis gets aligned to gravity after rotation instead of the z-axis.

## Slide 5: Linear Acceleration
Linear Acceleration virtual sensor data provides the measure of the acceleration of a device after removing the Gravity components on the 3-axes.
Accurate linear acceleration data can be calculated by subtracting gravity components from the 3-axes accelerometer data.
LAx = (Ax - Gx) / Gravity;
LAy = (Ay - Gy) / Gravity;
LAz = (Az - Gz) / Gravity;
Linear acceleration is measured relative to gravity. Example when phone is placed face-up, the linear acceleration is 0. When it is in free fall it goes to 1, and probably at escape velocity it should go to -1. This is done to have a range of -1 to +1 for linear acceleration.